## Slide 1: Hydro: A Hybrid Routing Protocol for Low-Power and Lossy Networks
Stephen Dawson-Haggerty, Arsalan Tavakoli, and David Culler
The University of California Berkeley

## Slide 2: Low Power and Lossy Networks
Diversity of applications: customer premise (into the home, “HANs”), neighborhood networks (ie, smart meters, “NANs”)
  Smart appliances, programmable lighting controllers & thermostats, building automation
United by common link properties: slow, low-power, lossy
  802.15.4e/g, PLC
IPv6 as a unifying framework
  6lowpan/ROLL working groups

## Slide 3: Building Information
CT: mains power monitoring
panel level power monitoring
ACme: plug load energy monitor and controller
3
Temperature
Humidity
Vibration
Pressure
Load Tree
Climate Plant
Operations and Environment

## Slide 4: The Routing Problem
Spatial and temporal variation in link quality
Limited resources bound state
  48KB ROM, 10KB RAM
Radio communication expensive
  Long-lived deployments require extensive duty-cycling

## Slide 5: IETF
6lowpan
  Adaptation layer for IPv6: 802.15.4 links
ROLL: Routing over Lossy and Low-Power Links
  Routing

## Slide 6: Can we quantify that?
Metric
Requirement
Table Scalability
Loss Response
Control Cost
Link Cost
Node Cost
# of Destinations
Limited to Active Path
Bounded by Data Rate
Link Dynamicity
Node Heterogeneity

## Slide 7: What do we really need?
Workload
Network Topology
Collection (MP2P) Traffic
Point-to-Point Traffic
Resource-Starved
More Capable Devices
Border Router
Node

## Slide 8: Our Solution: HYDRO
Two Components:
  Distributed DAG for underlying connectivity
  Centralized Controllers for Point-to-Point Optimization

## Slide 9: Our Solution: HYDRO
Trickle timers for DAG construction
  recognize local inconsistencies and quickly repair them
  when network is stable, control traffic peters out
Source routing for routes not along a DAG
  increased packet overhead
  loop freedom
Centralized topology view
  allows point-to-point and anycast optimizations

## Slide 10: Our Solution: HYDRO

## Slide 11: Distributed DAG Formation
2
5
7
4
6
1
3
Router Advertisement
Route Cost
Willingness
Neigh | Route | Link | LQI | Conf
2 | 1.2 | MAX | 90 | 0
4 | 2.5 | MAX | 100 | 0
5 | 2.6 | MAX | 100 | 0
Default Route Table (Node 7)

## Slide 12: Distributed DAG Formation
2
5
7
4
6
1
3
Neigh | Route | Link | LQI | Conf
2 | 1.2 | 1 | 90 | 1
4 | 2.5 | MAX | 100 | 0
5 | 2.6 | MAX | 100 | 0
Default Route Table (Node 7)

## Slide 13: Distributed DAG Formation
2
5
7
4
6
1
3
Neigh | Route | Link | LQI | Conf
2 | 1.2 | 2 | 90 | 7
4 | 2.5 | 1.1 | 100 | 3
5 | 2.6 | MAX | 100 | 0
Default Route Table (Node 7)

## Slide 14: Distributed DAG Formation
2
5
7
4
6
1
3
Neigh | Route | Link | LQI | Conf
2 | 1.2 | 2 | 90 | 7
4 | 2.5 | 1.3 | 100 | 5
5 | 2.6 | 1.4 | 100 | 5
Default Route Table (Node 7)

## Slide 15: Global Topology Formation
2
5
4
6
1
3
Neigh | Route | Link | LQI | Conf
2 | 1.2 | 2 | 90 | 7
4 | 2.5 | 1.3 | 100 | 5
5 | 2.6 | 1.4 | 100 | 5
Neigh | Cost
2 | 2
4 | 1.3
5 | 1.4
7
Default Route Table (Node 7)

## Slide 16: Centralized Routing
2
5
4
6
1
3
7
Dest | Flow Path
6 | [4 1 6]
Neigh | Route | Link | LQI | Conf
2 | 1.2 | 2 | 90 | 7
4 | 2.5 | 1.3 | 100 | 5
5 | 2.6 | 1.4 | 100 | 5
D:6
DATA
D:6
DATA
[3 6]
D:7
[2 7]
RI [4 1 6]
D:6
DATA
[4 1 6]
Default Route Table (Node 7)
Flow Table (Node 7)

## Slide 17: Centralized Routing
2
5
4
6
1
3
7
Dest | Flow Path
6 | [4 1 6]
Neigh | Route | Link | LQI | Conf
2 | 1.2 | 2 | 90 | 7
4 | 2.5 | 1.3 | 100 | 5
5 | 2.6 | 1.4 | 100 | 5
D:6
DATA
[3 6]
D:7
[2 7]
RI [5 1 6]
D:6
DATA
[4 1 6]
D:6
DATA
[F4 1 6]
Default Route Table (Node 7)
Flow Table (Node 7)

## Slide 18: Centralized Routing
2
5
4
6
1
3
7
Dest | Flow Path
6 | [5 1 6]
Neigh | Route | Link | LQI | Conf
2 | 1.2 | 2 | 90 | 7
4 | 2.5 | 1.3 | 100 | 5
5 | 2.6 | 1.4 | 100 | 5
Default Route Table (Node 7)
Flow Table (Node 7)

## Slide 19: Outline
HYDRO
  Design Overview
  Evaluation
  Limitations
  Extensions / Discussion

## Slide 20: Evaluation Concerns and Metrics
Concern
How to Evaluate?
Reliability
Convergence
Stretch
Agility/Stability
Scalability
Packet Delivery Ratio
Global Topology View Progression
Transmission Stretch
Performance Under Node Churn
Larger Networks

## Slide 21: Test Environments
Name | Size | Diameter
Motescope | 49 | 4
Motelab | 128 | 8
ACME | 57 | 8

## Slide 22: Increased Concurrent Load
Decreases transmissions per success by about 1: ~ 25%
Lower PDR from congestion around Border Router

## Slide 23: Resilience to Failure
Network becomes partitioned
Failed nodes along default route

## Slide 24: IETF Criteria: How do we fare?
Criteria
Requirement
Table Scalability
Loss Response
Control Cost
Link Cost
Node Cost
# Destinations
Limit to Active Path
Bounded by Data Traffic
Link Quality Awareness
Heterogeneity
HYDRO
State for Active Flows
No explicit loss response
Driven by data traffic
ETX
Willingness and Node Attributes

## Slide 25: Limitations?
Mobility / Significant Dynamicity
Source Routing and Deep Networks
Single Point of Congestion and Failure

## Slide 26: Standards Implications
Early version presented to IETF
Working group: ROLL: Routing over Lossy and Low-Power Networks
  Rechartered in 2009 to design new routing protocol
Many design features represented in “final” version
  density-sensitive state propagation (trickle timers)
  “up and down” routing
  dynamic link estimation
Point to point does not include centralized optimization

## Slide 27: Questions?

## Slide 28: Backup Slides

## Slide 29: Centralized Routing
2
5
4
6
1
3
7
Dest | Flow Path
6 | [4 1 6]
Dest | Flow Path
7 | [1 4 7]
Neigh | Route | Link | LQI | Conf
2 | 1.2 | 2 | 90 | 7
4 | 2.5 | 1.3 | 100 | 5
5 | 2.6 | 1.4 | 100 | 5
D:6
DATA
D:6
DATA
[3 6]
RI [1 4 7]
D:7
DATA2
[1 4 7]
RI [4 1 6]
Default Route Table (Node 7)
Flow Table (Node 7)
Flow Table (Node 6)

## Slide 30: Extensions
Multicast
Hop-By-Hop Route Installs
More Complex Routing Policies
Levis et al. “The firecracker protocol”, ACM SIGOPS European Workshop

## Slide 31: State Management
2
5
4
6
1
3
7
Link State Database
Default Route Table
Paths for Active Flows
Paths installed in network
Utilization of installed paths
Utilization of Flow Tables
?

## Slide 32: Hypothesis
Hybrid Routing Solution
Centralized Control
Distributed Local Agility
Lossy and Low-Power Networks
Data Centers
Path-Level Decisions
Link-Level Decisions

## Slide 33: Existing Solutions??
Collection-Oriented Protocols
Point-to-Point Protocols
MintRoute
MultiHop LQI
CTP
Hui’s IP Architecture
BVR
OLSR
DYMO
S4

## Slide 34: Don’t Centralized Solutions Exist?
Existing Solutions
Inherent Assumptions
Routing Control Platform (RCP)
4D
SANE / ETHANE / NOX
Reliable Path to Centralized Controller
Consistent Global View of Topology
Reliable Links

## Slide 35: Low-Power and Lossy Networks (L2Ns)
Sensor equipped
Low-bandwidth wireless radio
Constrained resources
Limited energy reserves

## Slide 36: Global Topology Formation
Basic Connectivity achieved quickly

## Slide 37: Global Topology Formation
30-Second Interval
5-Minute Interval
Limited improvement in stretch beyond basic connectivity
Longer intervals drastically slow convergence

## Slide 38: Applications

## Slide 39: Distributed DAG Formation
57 Nodes
1 report / min
Channel 19
Methodology
Real Energy Deployment

## Slide 40: Multiple Border Routers
Second border router helps eliminate long paths