## Slide 1: sMAP – a Simple Measurement and Actuation Profile for Physical Information
Stephen Dawson-Haggerty, Xiaofan Jiang,
Gilman Tolle, Jorge Ortiz, and David Culler
Computer Science Division
University of California, Berkeley
© 2010 All rights reserved

## Slide 2
Physical data is everywhere
Information from the world
Timeseries
Buildings
Wed Oct 27 12:35:00 2010,92.8
Wed Oct 27 12:40:00 2010,91.6
Wed Oct 27 12:45:00 2010,92.76
Wed Oct 27 12:50:00 2010,89.445
Wed Oct 27 12:55:00 2010,95.0
Wed Oct 27 13:00:00 2010,94.005
Wed Oct 27 13:05:00 2010,96.3
Wed Oct 27 13:10:00 2010,91.61
Wed Oct 27 13:15:00 2010,97.475
Wed Oct 27 13:20:00 2010,95.825
BMS
Light
Transport
HVAC
Electrical
Perimeter HVAC
Core HVAC
Ambient Lighting
Task Lighting & Conditioning
Power Load Mgmt
Shade or Passive Solar
Natural Ventilation
Notes: What is physical, data, everywhere

## Slide 3: Why buildings?
72% of electrical consumption, 40% of total consumption, 50% with construction, 42% of GHG footprint
Commercial building consumption 2x 1980-2000, 1.5x more by 2025 [NREL]
Where the coal is used
The prime target of opportunity for renewable supplies
Renewable energy consumption
Electricity source

## Slide 4: Cyber / Physical Building
BMS
Cyber
Physical
Building
Light
Transport
Process Loads
Occupant Demand
Legacy Instrumentation & Control Interfaces
Pervasive Sensing
Activity/Usage
Streams
BIM
PIB
Activity Models
Multi-Objective Model-Driven Control
Building Integrated
Operating System
External
HVAC
Electrical
Fault, Attack, Anomaly Detect &Management
Control Plan and Schedule
Physical Models
Human-Building Interface

## Slide 5: “Smart Buildings”
BMS
Light
Transport
HVAC
Electrical
Protocol | Year | Network | Example Applications
Modbus | 1979 | RS-485, TCP/IP | Panel monitoring, alarms
Fieldbus/HART | 1988 | various | Industrial Control
BACnet | 1995 | ARCNET, Ethernet, IP, RS-232, etc. | HVAC, Lighting, Fire…
WirelessHART | 2007 | 802.15.4e | Industrial control, wire replacement
Zigbee SEP 2.0 | 2011? | 802.15.4 | Plug-load monitoring
HUGE installed/legacy base
Multiple generations of hardware and software in the same building
Typical integration: proprietary vertical Building Management System (BMS)
  Data in at the bottom
  Data products out at the top
Notes: Different types of sensors and systems in a building

## Slide 6
REST API
HTTP/TCP
…
JSON Objects
Electrical
Weather
Geographical
Water
Environmental
Structural
Actuator
Occupancy
sMAP
Modeling
Visualization
Continuous Commissioning
Control
Personal Feedback
Debugging
Storage
Location
Authentication
Actuation
Applications
Physical Information
Vertical Protocol Layering
What is “RSS” for physical data?
Make available diverse information sources
Support publishing to the Internet
Horizontal Architecture
Notes: Series of “of course” design decisions
- publishing
- diversity below and above

## Slide 7
Design goals
“Uniform” access to real-time
data from an instrument
Open data to a new class of
application developers
Dive in: application oriented design
RESTful: “representations of resources”
What resources, what do we “represent”?
Notes: REPLACE modbus, and all that
sMAP is not a database
a PARTICULAR protocol, not a generic framework

## Slide 8
Discover
GET /data
[“cory”]
GET /data/cory
[“sensor”, “meter”]
GET /data/cory/sensor
[“temperature”, “wind”, “humidity”]
GET /data/cory/sensor/temperature/reading
{ “Reading” : 23,
“ReadingTime” : 1288385832,
“ReadingSequence” : 123123 }
Access
Example sMAP Interaction

## Slide 9
Support three things: metering, sensing, actuation
Measuring: instantaneous values | Metering: accumulated values
i.e., temperature | i.e., electricity
Units | 
Conversion to Engineering Units | 
Other metadata (?) | 

## Slide 10
Identify sense points and channels
Sense points: physical point of instrumentation
i.e., the sensor; “the weather station”
Channel: single stream of scalars
“temperature”

## Slide 11
Map these to HTTP resources
/ # list resource under URI root [GET]
/data # list sense points under resource data [GET]
/ [sense_point] # select a sense points [GET]
/meter # meters provide this service [GET]
/ [channel] # a particular channel [GET]
/reading # meter reading [GET]
/format # calibration and units [GET/POST]
/parameter # sampling parameter [GET/POST]
/profile # history of readings [GET]
 Represent units, sampling parameters of the underlying
device, for each channel

## Slide 12
What else do we need?
Events
Embedded devices support

## Slide 13
Event Reporting: add “callbacks” to HTTP
POST /reporting/create
{ “Period” : 0,
“ReportResource” : “~/data/*/*/*/reading”,
“ReportDeliveryLocation” : “http://www.openbms.org/add/2133”
}
 Period “0” means only changes get pushed
Same semantics as a GET on ReportResource
Alternatives are “long get,” webevents/multipart HTTP style
Notes: Issues working through firewalls + NATS
the rest of the web is going with “long polling”, event-driven servers like twisted or tornado or other epoll-based mechanisms (libevent)

## Slide 14
Embedding sMAP
Emerging design pattern: define Internet-scale protocol, use adaptation layer where necessary
Edge Router
Edge Router
EBHTTP / IPv6 / 6LowPAN Wireless Mesh Network
sMAP
sMAP
sMAP
sMAP
Temperature/PAR/TSR
AC plug meter
Light switch
Proxy Server
EBHTTP Translation
Edge Router
Proxy Server
Avro
Translation
 Preserve extensibility and self-describing properties of JSON
 UDP transport option with stop-and-wait RETX
Notes: of COURSE you can run this over 6lowpan if you want – previous senSys results

## Slide 15
EBHTTP
Avro Encoding
GET /.schemas
HTTP 1.0 200 OK
Content-encoding: gzip
GET /data/*/*/*/reading
HTTP 1.0 200 OK
Content-type: application/avro
X-Avro-Schema: reading
Apache software foundation project for efficient serialization of JSON: documents reference a schema
Additional specification necessary to use it in a RESTful way
Pack HTTP into a binary message structure: TLV encode headers, body
Supports most HTTP features but over connectionless UDP: ideal for 6lowpan data collection networks
drives an architecture
Proxies for accessing end-devices needed for scalability, security anyways
Makes “end-to-end” possible again
Notes: - example of compression
- not application layer gateway
- similar to the CoAP approach being adopted in the IETF

## Slide 16
That’s it: keep it simple
no...
“external” metadata
data repository
credentials database
...anything not an instrument property
Google PowerMeter
Cell phone
EveryBuilding
Database
IPv6 / 6LowPAN Wireless Mesh Network
sMAP
sMAP
sMAP
sMAP
sMAP
Modbus
RS-485
sMAP
Internet
Notes: Only metadata intrinsic to the instrument: model is something you could ship, complete
the key thing is the application

## Slide 17
The sMAP library
15 different underlying sensors and stacks
More then 100 instruments, > 200 ACme plug-load meters
4400 channels of high-resolution data
  80 sMAP “instances”
  together 250 samples/sec
It’s easy: simplest service is ~3 lines of Python
Notes: Totally different underlying technologies
effectively hide legacy: mention SCADA,
There are other challenges but we solved this one
This is just from one group – everybody has the same problem, too
Also PGE data, SCADA system, Cluster
~100loc sometimes

## Slide 18: Dent Powerscout 18 sMAP Feed
/ # list resource under URI root [GET]
/data # list sense points under resource data [GET]
/[sense_point] # select a sense points [GET]
/meter # meters provide this service [GET]
/[channel] # a particular channel [GET]
/reading # meter reading [GET]
/format # calibration and units [GET/POST]
/parameter # sampling parameter [GET/POST]
/profile # history of readings [GET]
Sense Point | Description | Channels
A, B, C | Single-phase | real, apparent, reactive power + energy. power factor. current. phase-neutral voltage
AB, BC, AC | Phase-to-phase | voltage
ABC | Whole-circuit | real, apparent, reactive power + energy. power factor. current. phase-neutral voltage, line frequency
Notes: there are many other smap feeds like this
three phase panel meter

## Slide 19
Every deployment needs this
Shared Application: Visualization
http://www.openbms.org/smap/plot/2989/1

## Slide 20
Shared Application: Metadata Repository

## Slide 21
open source library
sMAP represents instruments
lots of independent tools on top
storage
metadata
authentication
location
and more from the community
sMAP
Dent circuit meter
sMAP
Temperature/PAR/TSR
sMAP
Dent circuit meter
sMAP
Temperature/PAR/TSR
Dent circuit meter
Temperature/
PAR/TSR
sMAP
sMAP
EveryBuilding
Archival
Notes: - represents instruments: and that is the boundary. drives a focus on data since at the end of the day it’s “just” sMAP,, no matter how it gets to you.
- open source: this stuff isn’t that much fun to develop, so we can share components
- the tools become more “portable” too since they accept the same data – out of scope but critical in managing a deployment
- everyone typically wants similar things for their deployments, so now if you just “smap” it, it plugs into the rest of the system. Very different from other deployments I’ve worked on with custom app gateways at the edge. That stuff is important too, but at the end of the day all you want is the data. represents a separation of concerns for application development. this is really just SoA.
- let’s do it 

## Slide 22: Thank You
http://www.openbms.org/
http://www.openbms.org/smap/plot
Internet
Cell phone
sMAP Gateway
sMAP
Modbus
RS-485
sMAP
sMAP Gateway
EBHTTP / IPv6 / 6LowPAN Wireless Mesh Network
sMAP
sMAP
sMAP
sMAP
Edge Router
Temperature/PAR/TSR
Vibration / Humidity
AC plug meter
Light switch
Dent circuit meter
Proxy Server
EBHTTP Translation
California ISO
sMAP Gateway
sMAP Resources
Applications
Google PowerMeter
Weather
sMAP
Every Building
Database